## Slide 1: Incorporating Reliability in SoC Flow
Aatmesh Shrivastava
Taniya Siddiqua

## Slide 2: Motivation
Technology Scaling
More Cores/ Larger Memories
Higher Performance
AMD Phenom™
Intel Nehalem™
IBM POWER7™
Moore’s Law
Abstraction of Reliable Hardware

## Slide 3: Silicon Reliability
EM
NBTI
PBTI
TDDB
Implement DFR to Ensure Long-term Reliability

## Slide 4: Negative Bias Temperature Instability (NBTI)
Interface traps
‘1’
‘0’
Negative bias
Increases Vt and circuit delay
Causes processor failure
‘1’
‘1’
Recovery phase
No bias
Restores Vt
Improves delay

## Slide 5
Hot Carrier Injection

## Slide 6: Goals
Develop reliability spice models from literature.
Develop methodology to assess the reliability of the circuit.
Obtain the critical paths and characterize it for worst case.

## Slide 7: Top-level Flow
Timing Analysis
Generate Netlist
RTL Design
Transistor Model
Std. Cell Degradation
Model
F(t,α,vdd,T,l)
Critical Path
Reliability assesment
Obtaining WC Performance

## Slide 8: Transistor Reliability Model
G
D
S
VGS  (VDD)
VDS  (VDD, fan_out)
Temp  (Temp)
Time  (year, activity)
Modeling component
  VDD
  fan_out
  Temp
  Year
  Activity

## Slide 9: Transistor Reliability Model
By using MOSRA degraded transistor model can be obtained.
However, MOSRA never ran properly.
We constructed our own device model using PTM from ASU. http://ptm.asu.edu/
R. Vattikonda DAC 06
From the implemented Model

## Slide 10: Standard Cell Model
VDD, Temp and fanout were varied and there delay at time 0 was calculated for a given std. cell.
Device degradation at the given VDD, Temp. and fanout was calculated by further varying activity and time.
This will result in ΔVth for each particular corner.
Using this we can calculate delay degradation for each particular corner.
We can use the obtained degraded delay to construct the reliability model for std. cell as a function of 5 variables.

## Slide 11: Standard Cell Model ctd.
Varying only activity.
Delay was obtained for 10 different activities.
2nd order polynomial is a good approximation.
Which gives us a function to directly map activity to delay.

## Slide 12: Standard Cell Model ctd.
Varying only stress time.
Delay was obtained for 10 different time.
2nd order polynomial is a good approximation.
Which gives us a function to directly map stress time to delay.

## Slide 13: Standard Cell Model ctd.
Combining stress time and activity considering everything else being constant
9 variables a, b, …k needed to construct the model
By using 9 different points w.r.t activity and time a, b,.. Can be obtained
Matlab can be used to solve this
TDG= (a1*t2+b1*t+c1)*(a2*α2+ b2*α+c2)
TDG=a*t2*α2+b*t*α2+c*α2 + d*t2*α+e*t*α+ f* α+g*t2 +h*t+k

## Slide 14: Standard Cell Model ctd.
Coefficients were obtained using the explained procedure.
Model was constructed
Maximum Error 0.5%

## Slide 15: Standard Cell Model
Proceeding this way dependence on other 3 parameters VDD, Temp and fanout can be established.
Advantages of this model
  While we are presenting the solution in the context of reliability, the equation with P, T and V can easily be established for any standard cell.
  Potential to replace .libs
  Having delay or other characteristics in the form of equation can provide great flexibility in terms of library creation and accounting for cross domain analysis, etc, can enable DVFS in SOC flow.
Since VDD, Temp and fanout are more static than others, we kept the model at this level only.
For each combination of VDD, Temp and fanout, the 9 variable matrix was evaluated.

## Slide 16: Standard Cell Model
Applying the preceding procedure models for each standard cell can be constructed in the similar fashion
However similarity in the std. cell architecture can be leveraged.
Each standard cell essentially has push-pull structure like inverter, so they are likely to degrade in the similar fashion.
To evaluate this we obtained the relative delay of both inverter and other standard cell and compared.

## Slide 17: Standard Cell Model
Maximum Error 15%
Since the errors were in the range of 15% we chose to use the one model normalized to t=0 delay for each cell.
This was done to reduce the effort. For more accuracy model can be constructed for each std. cell.

## Slide 18: Top-level Flow
Timing Analysis
Generate Netlist
RTL Design
Transistor Model
Std. Cell Degradation
Model
F(t,α,vdd,T,l)
Critical Path
Reliability assesment
Obtaining WC Performance

## Slide 19: Obtaining the Critical Path
We use PrimeTime, the Synopsys static timing analysis (STA) tool
PrimeTime performs full-chip static timing analysis with high speed and low memory utilization
Steps:
  read a design
  link a design to libraries
  establish constraints on the design (e.g. electrical loading rules)
  specify environmental attributes
  perform timing analysis.

## Slide 20: PrimeTime Requirements
Verilog description should be either a gate-level database file (.ddc) or a Verilog file generated by Design Compiler (the Synopsys synthesis tool)
Failing to observe this will lead to 0 delay paths when you execute report_timing
Such modules are treated as "black boxes" with no timing arcs, as the system appears to ignore the library cell delays if the modules use position association instead of name association

## Slide 21: Design Compiler
read_verilog ./risc_core.v
analyze -library WORK -format verilog {./risc_core.v}
elaborate RISC_CORE -architecture verilog -library DEFAULT
link
check_design
compile -exact_map
write -hierarchy -format verilog -output ./results/RISC_CORE.v

## Slide 22: Design Constraints File
# Define a clock for synchronous design (constrains all register to register timing paths)
# Required: Clock source, Clock period. Options: Duty cycle, offset/skew, clock name
create_clock -period 9 [get_ports Clk]
# Constrain input and output timing paths
set_input_delay -max 1.5 -clock Clk [all_inputs]
set_output_delay 1 -clock Clk -clock_fall -max [all_outputs]
# To specify the fastest arrival time of the external logic to the input ports:
set_input_delay –min 0.25 –clock –Clk [get_ports A]
# To specify the hold time of the external logic on the output ports of the design:
set_output_delay –min –0.25 –clock Clk [get_ports C]
set_wireload_model “enclosed”
set_operating_conditions WORST

## Slide 23: PrimeTime
  set search_path ../ref/models
  set link_path “* ../ref/models/saed90nm_type.db”
  set link_create_black_boxes false
  read_verilog /path_to_your_design/source_file_name
  link_design –keep_sub_designs $DESIGN_NAME
  check_timing
  source ./constraints/constraint_file_name.tcl
  report_path_group > reports/${DESIGN_NAME}.path_group
  report_timing > reports/${DESIGN_NAME}.timing
  report_timing -max_paths 10

## Slide 24: Critical Path
Point Incr Path
I_INSTRN_LAT/Crnt_Instrn_1_reg[27]/Q (DFFX1) 0.41 0.41 r
I_ALU/U15/ZN (INVX0) 0.29 0.70 f
I_ALU/U4/ZN (INVX0) 0.44 1.14 r
I_ALU/U516/Q (OR2X1) 0.38 1.52 r
I_ALU/U515/QN (NOR2X0) 0.13 1.66 f
I_ALU/U509/ZN (INVX0) 0.33 1.99 r
I_ALU/U479/QN (NOR3X0) 0.33 2.32 f
I_ALU/r24/U1/Q (XOR2X1) 0.25 2.57 f
I_ALU/r24/U1_0/CO (FADDX1) 0.34 2.91 f
I_ALU/U270/Q (MUX21X1) 0.17 8.60 f
I_ALU/U216/Q (AND2X1) 0.13 8.73 f
I_ALU/U223/Q (MUX41X1) 0.26 8.99 f

## Slide 25: Critical path degradation
DFF (0.41) => INV (0.29) => INV (0.44) =>
OR2 (0.38) => NOR2 (0.13) => INV (0.33) =>
NOR3 (0.33) => XOR2 (0.25) =>
FADD (0.34) => FADD (0.34) => FADD (0.34) => FADD (0.34) =>
FADD (0.34) => FADD (0.34) => FADD (0.34) => FADD (0.34) =>
FADD (0.34) => FADD (0.34) => FADD (0.34) => FADD (0.34) =>
FADD (0.34) => FADD (0.34) => FADD (0.34) => FADD (0.34) =>
FADD (0.37) =>
XOR2 (0.22) => MUX21 (0.16) => MUX21 (0.17) => AND2 (0.13) => MUX41 (0.26) => AO22 (0.17) => DFF (0.04)
The critical path degrades from 9.52ns to 10.35ns after 5 yrs.
We obtain this using the flow and model.

## Slide 26: Summary
Develop reliability spice models from literature.
  MOSRA never ran properly.
  We constructed our own device model
Develop methodology to assess the reliability of the circuit.
Obtain the critical paths and characterize it for worst case.
  Used PrimeTime Static Timing Analysis